## Slide 1
FPGA-Based Morse Code Communication System
CE436 – Digital System Design | Complex Engineering Problem (CEP)
Platform: Digilent Nexys A7 (100 MHz FPGA)
Ahmad Mir 2022062
Abubakar Mazhar 2022039
Aqeeb Warriach 2022349

## Slide 2
Project Objectives and Scope
Core Functionality
Design an FPGA-based system to accurately encode decimal digits (0–9) into standard Morse code elements.
Operational Modes
Implement support for single-digit transmission utilizing on-board switches and buttons.
Timing Fidelity
Achieve precise, real-time timing control and sequencing, leveraging the 100 MHz FPGA clock source for maximum accuracy.
Hardware Target
Ensure successful synthesis, mapping, and physical implementation on the Digilent Nexys A7 FPGA development board.

## Slide 3
Design Methodology: Architecture and Control
FSM-Centric Control
The entire sequencing and timing generation is managed by a central Finite State Machine (FSM).
Decoupled control logic facilitates modular testing and verification.
Deterministic timing is derived from the master 100 MHz clock using counter logic.
Modular RTL Design
Each functional block (Debouncer, FIFO, FSM, Timing) was implemented as a separate, verifiable RTL module.
Used VHDL/Verilog for hardware description, ensuring optimized resource utilization on the A7 FPGA.

## Slide 4
System Architecture: Block Diagram
The system is comprised of six primary modules, ensuring robust input handling, deterministic encoding, and precise output signaling.
Input
Switches & Buttons
Preprocessing
Debounce & FIFO
Core Logic
Morse LUT & FSM
Output
LED & 7-Segment

## Slide 5
FSM and Deterministic Timing Control
Finite State Machine (FSM) States
IDLE
Awaiting input trigger.
FETCH_DIGIT
Retrieving next digit from FIFO.
LOAD_PATTERN
Accessing Morse pattern via LUT.
SEND_ELEMENT
Active transmission (Dot/Dash).
ELEMENT_GAP
Short pause between elements.
DIGIT_GAP
Longer pause between digits.
DONE
Transmission complete.
Timing Rules (Unit Time 't' = 0.5s)
Dot Duration
2t (1.0 second)
Dash Duration
6t (3.0 seconds)
Element Gap
1t (0.5 second)
Digit Gap
4t (2.0 seconds)
These rules are strictly based on standard Morse code conventions, with timing scaled for visual clarity.

## Slide 6
Verification: Simulation Results
Extensive simulation was performed to ensure precise FSM sequencing and accurate timing before hardware synthesis.
Testbench Strategy
Verified single-digit FSM flow, confirming 1:3 ratio for Dot:Dash durations.
Multi-digit verification confirmed FIFO handling and correct sequencing of Digit Gap between transmissions.
Accelerated simulation timing (reduced clock speed) was used to compress waveform visualization.
Simulation Waveforms :
The clock, FSM state transitions,
and LED output signal can be seen
demonstrating the correct timing sequence.

## Slide 7
Hardware Implementation and Results
The synthesized design was successfully deployed to the Nexys A7, validating the real-world performance of the system.
Successful Synthesis
The design met all timing constraints and utilized resources efficiently, confirming RTL quality.
Real-Time Operation
Observed LED output timing confirmed simulation results, demonstrating accurate real-time response to input changes.
Interface Validation
Physical input from switches and buttons was robustly handled by the debouncer module.
Explicit Placeholder for FPGA Board Photos
Photos should showcase the Nexys A7 board with visible connections and the output LEDs/7-segment display.

## Slide 8
Live FPGA Demonstration
The following demonstration showcases the system's core functionality, highlighting robust input handling and accurate Morse output timing.
Live Demo / Video Placeholder
Test 1: Single Digit
Entering a digit (e.g., '0') and verifying the 5-dash sequence.
Test 2: Multi-Digit Mode
Entering a number (e.g., '42') and observing the correct digit spacing.

## Slide 9
Challenges and Engineering Lessons Learned
The project provided critical experience in bridging theoretical digital design with practical hardware constraints.
Precise Timing Control
Mastering clock division techniques to derive multi-second timing from a 100 MHz source was the key challenge.
Asynchronous Inputs
Understanding the necessity of synchronization and debouncing circuits for reliable interaction with physical buttons and switches.
FSM Sequencing
Implementing robust state transitions to handle the varying length of Morse patterns and multi-digit sequencing proved complex but rewarding.
Modular Design Value
Confirmed that well-defined RTL modules significantly simplify verification, integration, and debugging in a large system.

## Slide 10
Conclusion and Future Work
We successfully implemented a fully functional, robust, and accurate FPGA-based Morse code encoder, meeting all CEP requirements.
Project Summary
Achieved accurate, deterministic timing behavior.
Validated design via comprehensive simulation and successful hardware deployment.
Demonstrated strong alignment with CEP objectives through complex system integration.
Next Steps: Expanding Capability
Full Alphabetical Support
Extend the Morse LUT and FSM to include letters (A-Z) and punctuation.
Alternative Outputs
Implement Audio tone generation or UART transmission capability.
Wireless Communication
Integrate a transmission module (e.g., XBee) for short-range wireless Morse broadcasting.